## Slide 1: Intel Engineers ECE 3992
Semrah Odobasic, Logan Allen, Jin Jeong

## Slide 2: Agenda
The Project
  Overview of the entire project
Risk Assessment & Progress
  LED Matrix Library
  Blender Data
  Display 3D Data on Matrix
  Assembly of Prototype
Future Plans / Stretch Goals
  Different Technologies
  Augmentations to Current Design

## Slide 3: The Project
Volumetric 3D Display
  Microcontroller
  LED Display
  Motor
  Motor Driver
  IR Sensor
  Battery
Blender Data
  24 2D Frames per 3D Frame
  Displayed based on RPM

## Slide 4: Convert display library to C High Risk [Completed]
AdaFruit IS31FL3731
  Python Library
    Inexperience with Python
    Dislike of the Python IDE/toolchain
  C++ Library
    Involves Two Languages
    Cross Compilation Required
Our C Library
  Formatted for the Raspberry Pi Pico
  Integrates Pico I2C with the Display Library

## Slide 5: Motor Control Low Risk [Complete]
Motor Control via Motor Driver Board
  Ensures no limits are passed on the RP2040
  Motor can go Different Directions and Different Speeds Depending on PWM
Uses More Space
  Extra board required which is the same size as the RP2040
  Two H-Bridges but we only use one

## Slide 6: RPM Using IR Sensor Low Risk [Complete]
Ensures Display Switches Frames
  Which makes sure the image is stationary
  Display and IR sensing are done on two different cores to ensure they don't interfere with each other.
Falling Edge Detection
  Interrupt is triggered on a falling edge
  Interrupt counts the system time between the last call to determine the RPM

## Slide 7: Combine Everything Into Volumetric Display Medium Risk [In-Progress]
Assembly
  3D Printed Holder
    Supports Matrix
    Ensures Assembly Can Spin at High Speed
  Interconnection of All Systems
    We have Successfully Interconnected all Subsystems Together

## Slide 8: Intel Engineers ECE 3992
Semrah Odobasic, Logan Allen, Jin Jeong

## Slide 9: Extract 3D Data from Blender Medium Risk [Completed]
Blender Data Collection
  Animate and Render Frames
  Color Ramp Images for Pixels
  16 x 9 Resolution
Image to C Array
  Take in Blender Image
  White Pixels = 1 Black Pixels = 0
Save Array to Pico
  Consider Memory Limitations
  24 2D Frames to Make 3D image
Animated 3D Frames
  Very Manual Process

## Slide 10: Display 3D Data to LED Matrix Medium Risk [In-Progress]
Update Animation Based on RPM
  Matrix Switches Frames 24 Times a Rotation
  Pico uses the IR sensor RPM to Change Speed
In Progress
  Matrix switches based on RPM correctly
  Current Image is not Fully Accurate
    Most Likely from Rotation of Cube in Blender
  Rework Blender Animation for an Easier Image

## Slide 11: Future Plans | Stretch Goals
Different Style of Volumetric Display
  Swept-Volume Display (Current)
  Static Volumetric Display
    No Moving Parts
    LEDs preplaced in 3D Space
    Lasers in a Gas
Augment Current Design
  Bigger Display
  Bigger Motor
  RGB
Many More Possibilities
  Still Need to Think About it